## Slide 1: Accuracy effects of particle count and max step sizes
Daniel Fu, 2/18/2024

## Slide 2: Setup
Parameters considered
  Particle count, N
  Max step in vacuum (not in wedge)
  Max step in wedge
Technical note: G4Beamline has a global parameter “maxStep” and the wedge has its own “maxStep” value that overrides the global value
Graphs were generated by running each simulation 30 times with a 4-sigma cut and graphing the mean and standard deviation. The optimized 145μm parameters (145_new.pkl) were used for these tests.
As each parameter was varied, the others were left at default values of N=20000, max step in vacuum=0.5mm, max step in wedge=0.1
Code is in accuracy.py

## Slide 3: Number of particles

## Slide 4: Max step in vacuum

## Slide 5: Max step in wedge

## Slide 6: Conclusions
Simulation is stable in number of particles
  Higher particle counts reduce error
  Simulation time is linear in particle count (as expected)
Simulation is stable with max step in vacuum up to 10mm
Several graphs show sharp downward trends when max step in wedge increases beyond a certain point
  Occurs around 0.5 mm in xemit and yemit and around 0.1 mm in zemit
  Momentum mean and std show general trends that may be more concerning (but are within error ranges)
Previous simulations have been run at max step in vacuum = 0.5mm and max step in wedge = 0.1mm
  To improve speed, the max step in vacuum can probably be increased to 1-2mm without accuracy loss
  Max step in wedge should probably be left at 0.1mm