## Slide 1: Final Cooling Technique with Thick Wedges
Daniel Fu, University of Chicago
Diktys Stratakis and David Neuffer, Fermilab
11/30/2023

## Slide 2: Introduction
Final cooling is a major problem for development of a muon collider
Conceptual method for final cooling proposed by Neuffer in 1612.08960
We demonstrated feasibility and optimized design using simulation

## Slide 3: Proposed Final Cooling Concept
Beam passed through a thick wedge, which cools beam in one transverse axis through emittance exchange
Drift channel to build up correlation between time and momentum
RF cavity reduces momentum spread through phase rotation
Beam passed through second wedge to cool in second transverse axis

## Slide 4: Simulation Methods
Input distributions based on intermediate stages of high-field solenoid cooling channel
Considered two initial transverse emittances
G4Beamline used to simulate wedge and phase rotation process
Source: 1612.08960

## Slide 5: Parameters Considered
Wedge geometry
  Half-angle
  Length
Initial beam parameters
  Momentum
  Momentum spread
  Emittances
  Twiss parameters (beta, alpha)
RF cavity parameters
  Drift channel length
  Frequency
  Gradient
  Phase

## Slide 6: Optimal geometries for wedges
Determined optimal length and half-angle of first and second wedges to minimize output transverse emittance
Notes: These graphs were generated for the 145 um case

## Slide 7: Effects of β
Decreasing β (stronger focusing) reduces emittance growth in longitudinal and non-cooling transverse axes
Does not significantly affect emittance in cooling axis

## Slide 8: Effect of Momentum
Reducing momentum improves cooling
Does not affect emittance in non-cooling axis

## Slide 9: Effect of Momentum Spread
Decreasing momentum spread increases cooling
Optimal wedge angle correlated with initial momentum spread
Optimal wedge length unaffected

## Slide 10: Effect of Drift Length
Higher drift length makes phase rotation more effective
16m chosen as longest practical length

## Slide 11: Effect of RF cavity parameters
Optimal frequency is lower, 25 MHz chosen as lowest practical frequency
Optimal gradient and cavity length determined

## Slide 12: Phase-space diagram of cooling process

## Slide 13: Results
Achieved lower transverse emittance than previous best results
Demonstrated cooling from first and second wedges

## Slide 14: Assumptions and Caveats
Dispersion removal, drift channel, and focusing lattice not designed, idealized versions assumed (previous results are best-case)
Only longitudinal behavior was considered in the RF cavity
Possibility of refocusing before second wedge (potential for further performance improvement)

## Slide 15: Next Steps
Reduce assumptions described on previous slide, specifically by designing and simulating the magnetic components
Further optimize design to achieve equal cooling from second wedge
Characterize effect of changing multiple variables (potentially with high-performance computing)

## Slide 16: (additional slides follow)

## Slide 17: Optimized Channel Statistics

## Slide 18: Summary of Variables Considered
Variable | Status
Wedge geometry (half-angle and length) | Optimal values determined
Initial beta | As low as possible; 3.0 used
Initial alpha | Optimal value estimated at 0.7
Initial momentum | As low as possible; 100 MeV/c used
Initial momentum spread | As low as possible; 0.8-1.0 MeV/c used
Drift length | As long as practical; 16m used
RF frequency | 25 MHz used, optimal value is lower
RF gradient and length | Optimal values determined

## Slide 19: Effects of α
Increasing α decreases growth of emittance in longitudinal and second transverse axes (similar to decreasing beta)
Past around 0.5, increasing α decreases wedge performance (minimum transverse emittance increases)